## Slide 1: APOD
Using bluetooth/wireless designing and making a Lynxmotion A-Pod robot controller

## Slide 2: Embedded System – Team 3
Team Member:
  Phan Anh Dũng Cường – Team Leader
  Nguyễn Minh Quân – Team member

## Slide 3: ROBOT
10
Years ago

## Slide 4
+

## Slide 5
types of robot today.
5 main types
Walking Robots
Flying Robots
Wheeled Robots
Snake Robots
Wall Climbing Robots
Over 100,000

## Slide 6: Robot
Therapeutic
Industrial
Military
Education
Research

## Slide 7: Robot’s Density World Map

## Slide 8: INTRODUCE

## Slide 9
Introduce
  Hexapod
  Apod
What’s Include?
  Servos
  Modules Control
    SSC32
    STM32F4
  PC Control Interface
How’s difference?
  What did they do?
  What did we do?
How do we do?
  Algorithm
Demo
Pros and cons
Are there anything to be programmed in the future?

## Slide 10: Hexapod
A hexapod robot is a mechanical vehicle that walks on six legs. Since a robot can be statically stable on three or more legs, a hexapod robot has a great deal of flexibility in how it can move.
Many hexapod robots are biologically inspired by Hexapoda locomotion.
Uses:
  Test biological theories about insect locomotion.
  Motor control.
  Neurobiology.

## Slide 11: World of Hexapods

## Slide 12: What is our project?
Hexapod
APOD

## Slide 13: Apod
This is 3DOF hexapod
Prototype of incest robot
Include:
  6 legs
  1 head with Gripper
  1 tail
  1 body
25 Servos
3 Servos/ Leg
3 Servos
Vertical
Horizontal
Rotate
2 Servos

## Slide 14: Their Apod
SSC32
BOTBOARD II

## Slide 15: Their Apod

## Slide 16: Our Apod
SSC32
STM32F4

## Slide 17: Servos
Control System: +Pulse Width Control 1500usec Neutral
Required Pulse: 3-5 Volt Peak to Peak Square Wave
Operating Voltage: 4.8-6.0 Volts Operating Angle: 45 Deg. one side pulse traveling 400usec

## Slide 18: How’s Servo works?

## Slide 19: Type of Movement

## Slide 20: Module Control
SSC32
STM32F4 DISCOVERY

## Slide 21: SSC32
Microcontroller = Atmel ATMEGA168-20PU
EEPROM = 24LC32P (Required for 2.01GP)
Speed = 14.75 MHz
Internal Sequencer = 12 Servo Hexapod (Alternating Tripod)
Serial input = True RS-232 or TTL, 2400, 9600, 38.4k, 115.2k, N81
Outputs = 32 (Servo or TTL)
Inputs = 4 (Static or Latching, Analog or Digital)
Current requirements = 31mA
PC interface = DB9F
Microcontroller interface = Header posts
Servo control = Up to 32 servos plug in directly
Servo type supported = Futaba or Hitec
Servo travel range = 180°
Servo resolution = 1uS, .09°
Servo speed resolution = 1uS / Second
Servo motion control = Immediate, Timed, Speed or Synchronized.
PC board size = 3.0" x 2.3"
VS current capacity = 15 amps per side, 30 amps maxm

## Slide 22: SSC32

## Slide 23: SSC32

## Slide 24: STM32F4
STM32F407VGT6 microcontroller featuring 32-bit ARM Cortex-M4F core,
1 MB Flash, 192 KB RAM in an LQFP100 package
Board power supply: through USB bus or from an external 5 V supply voltage
External application power supply: 3 V and 5 V
LIS302DL or LIS3DSH ST MEMS 3-axis accelerometer
MP45DT02, ST MEMS audio sensor, omni-directional digital microphone
CS43L22, audio DAC with integrated class D speaker driver

## Slide 26: PC INTERFACE

## Slide 27: Sequence Player

## Slide 28: Configuration

## Slide 29: How’s difference?

## Slide 30: What did they do?
Apod (ONLY MANUAL CONTROL)
  Movement (Left, Right, Forward, Backward, etc.)
  Grip
  Lift
  Drop
  Some crazy action
Controller
  Using Wireless controller (2.4Ghz) direct connect with BOTII module
Brain
  All algorithm embedded in BOTBOARD II
Another function
  NONE

## Slide 31: What did they do?
(Video here)

## Slide 32: What did we do?
Apod (MANUAL AND AUTOMATIC)
  Movement (Left, right, forward, backward, etc.)
  Grip
  Lift
  Drop
  Some crazy action
Controller
  Using Bluetooth connect indirect through Pc interface, communicate with STM32F4
Brain
  All algorithm embedded in STM32F4 discovery

## Slide 33: What did we do? (cont)
Another function
  Live camera with detect color
  Automate redirect movement
  Automate indentify distance between Apod and the item

## Slide 34: Does we similar with others?
Built all implement from the begin
  Firmware (SSC32)
  Alternate module (STM32F4)
Just:
  Depend on Algorithm which World’s done to create function
NO

## Slide 35: What did we do? (cont)
Clip here

## Slide 36: How do we do?

## Slide 37: Forward

## Slide 38
APOD Flowchart

## Slide 39
SSC32 Flowchart

## Slide 40
STM32F4 Flowchart

## Slide 41: Demo

## Slide 42: Pros and cons
Short time to program
Hard to find hardware

## Slide 43: Are there anything to be programmed in the future?
Automate in movement like the insect
Tracking function and find the way to return
Can hear and make some dancing in music
Able to walk on stair
Obey (can follow the owner, hear the order of owner, etc.)

## Slide 44: END